## Slide 1: Network address Translation
Ammar khan
17010020010
BSCS-10

## Slide 2: The Problem
What is the problem?
Exhaustion of IPv4 address space
Who has this problem?
Internet Service Providers
Why should this problem be solved?
To be able to connect more devices to the internet

## Slide 3: Background Information
What is NAT?
  method of remapping one IP readdress space into another by modifying network address information in the IP header of packets while they are in transit across a traffic routing device mapping one IP.
  hides an entire IP address space, usually consisting of private IP addresses, behind a single IP address in another, usually public address space. The hidden addresses are changed into a single (public) IP address as the source address of the outgoing IP packets so they appear as originating not from the hidden host but from the routing device itself.

## Slide 4: Use cases
Single Public IP
A whole network of many networks with many devices ready to talk to internet can be addressed with 1 public IP.
Restricted Access
It selective access of the outside world to the inside NAT network as it only open ports on request of the device.
Encapsulation
Whole network inside NAT in such a way that outside world only sees the public IP and will never know of the details of inside device making the request.

## Slide 5: Types of NAT
STATIC NAT
DYNAMIC NAT
PORT ADRESS TRANSLATION

## Slide 6: STATIC NAT
Static NAT (Network Address Translation) is one-to-one mapping of a private IP address to a public IP address. Static NAT (Network Address Translation) is useful when a network device inside a private network needs to be accessible from internet.

## Slide 7: DYNAMIC NAT
Dynamic NAT can be defined as mapping of a private IP address to a public IP address from a group of public IP addresses called as NAT pool. Dynamic NAT establishes a one-to-one mapping between a private IP address to a public IP address. Here the public IP address is taken from the pool of IP addresses configured on the end NAT router. The public to private mapping may vary based on the available public IP address in NAT pool.

## Slide 8: PORT ADDRESS TRANSLATION
Port Address Translation (PAT) is another type of dynamic NAT which can map multiple private IP addresses to a single public IP address by using a technology known as Port Address Translation.
Here when a client from inside network communicate to a host in the internet, the router changes the source port (TCP or UDP) number with another port number. These port mappings are kept in a table. When the router receive from internet, it will refer the table which keep the port mappings and forward the data packet to the original sender.